## Slide 1: ST PASA Replacement Project
Stakeholder Meeting (30 Nov 2021)

## Slide 2: Agenda
Objective of Project
Progress to date
Stakeholder feedback
Latest indicative timetable
Appendix A (Refresh of Proposed design)
Appendix B - Conceptual Architecture

## Slide 3: ST PASA Replacement Project
Objective: To do a holistic review of the PD/ST PASA methodology and develop a system that would serve the NEM now, and into the future.
Details and updates can be found on ST PASA Webpage

## Slide 4: Progress to date
Phase 1 completed
  Initiate Industry consultation
  High level business requirements
  High level design (HLD)
  Proof of Concept (PoC)
  Conceptual Architecture Document (CAD)

## Slide 5: Progress to date
  Phase 2A commenced
  Tasks progressing in parallel
      Development of detailed business requirements
      Further development of uncertainty margins
      RFP for the SCED and load forecasting module
      AEMC Rule Change Consultation

## Slide 6: Business Requirements
    Project team developing business requirements for the full ST PASA process
    Formal procedure consultation with external stakeholders to commence early in 2022. The procedures include
      ST PASA Process description
      Reserve Level Declaration Guidelines (RLDG)
      Reliability Standard Implementation Guidelines (RSIG)
      Spot Market Timetable (for frequency of PASA runs)

## Slide 7: Forecasting: Uncertainty Margins
The use of Uncertainty Margins to reflect uncertainties in load forecasts, VRE forecasts and scheduled unit forced outages is described in the High Level Design (HLD)
A methodology to produce Uncertainty Margins is being developed. This methodology will be assessed as part of the next phase of the project.
  Details of the methodology and the assessment will be discussed with all stakeholders during the consultation phase. This information will assist in determining appropriate initial confidence levels, used to calculate the Uncertainty Margin.

## Slide 8: Request For Proposal (RFP)
  RFP for the SCED and Load Forecasting module
  SCED – Security Constrained Economic Dispatch (See Appendix B)
  Load Forecasting Module – to disaggregate zonal load forecasts to nodal load forecasts
  RFP developed and sent out on 9th Aug 2021
      Closed 24th Sept 2021
      Progressing selection of vendor/s and understanding timelines

## Slide 9: AEMC Rule Change consultation
  Rule Change proposal submitted (28th June 2021)
  AEMC submissions closed (23rd Sep 2021)
  Draft determination expected on 2nd Dec 2021
  The Rule change can be found on AEMC’s website here

## Slide 10: Stakeholder Feedback Themes
  Broadly support implementing changes to ST PASA and covering a 7-day period
  Support of publication of available capacity and PASA availability at a DUID level, except for one stakeholder who suggested this may result in incentives to exercise market power
  Support change of PASA availability definition to allow for more flexible recall times
  Mixed views on a principles-based approach to the Rules and including details in consulted on procedures. Several participants suggested the ST PASA procedure needs ‘full’ rules consultation

## Slide 11: Stakeholder Feedback Themes
  Suggestions that ST PASA is and will be overly conservative and trigger ‘early’ RERT intervention
    LOR triggers too conservative
    Should cater for demand side response in determining reserve
    Using Uncertainty Margin as input is double-counting
  PASA availability is confusing and difficult to use
  ST PASA modelling methodology be publicly available
  Suggestions that AEMO had disregarded “constructive criticisms” in its stakeholder consultation

## Slide 12: AEMO’s submission to AEMC consultation paper
In response to stakeholder feedback, AEMO’s submission to the AEMC’s consultation paper provided further clarifications:
  Scenarios demonstrating PASA availability and recall periods
  How lack of reserve (LOR) conditions relate to ST PASA re-development
  Full rules consultation to the development of procedures and the ability to have a full or single stage approach to future procedure changes

## Slide 13: Rule Change: PASA Availability and Recall time
Recall time to be flexible instead of fixed 24 hours
Range of allowable recall time to be defined in the RSIG
  Considering between 30 minutes and 72 hours
Recall time to be provided for each trading interval for the corresponding PASA Availability value
Submitted via the normal bids
Considering removing the Gen recall portal to reduce duplication of work
  Need to consider if need to keep the ability to submit two tranches of recall capacity and associated recall time

## Slide 14: Recall time scenarios
Scenario 1
300 MW unit OOS for maintenance
Require 72 hours’ notice on first day, 5 hours’ notice on the last day
Trading Interval | Max Availability (MW) | PASA Availability (MW) | Recall Period
1 | 0 | 300 | 72 hours
2 | 0 | 300 | 72 hours
… |  |  | 
Last day | 0 | 300 | 5 hours
 | 0 | 300 | 5 hours
Scenario 2
  300 MW unit partially unavailable
  Require 40 hours’ notice to return to full capacity
Trading Interval | Max Availability (MW) | PASA Availability (MW) | Recall Period
1 | 200 | 300 | 40 hours
2 | 200 | 300 | 40 hours
Scenario 3
  300 MW unit fully available
  Bid lower for commercial or other reasons
  Can return to full capacity in 30 minutes
Trading Interval | Max Availability (MW) | PASA Availability (MW) | Recall Period
1 | 150 | 300 | 30 minutes
2 | 200 | 300 | 30 minutes

## Slide 15: Use of PASA Availability
Max Availability – either technical or commercial capacity available for dispatch
PASA Availability – technical capacity that can be made available for PASA with x hours of notice (presently upto 24 hours)
AEMO exploring the appropriate use of Max Availability versus PASA Availability in PD/ST PASA
Potentially could produce results using both
  Max Avail – reserve conditions if there is no market response
  PASA Avail – to show how much market response is available (potentially, at a cost) for a forecast reserve condition
To be further explored during procedures consultation

## Slide 16: LOR/Intervention levels (TBD)
Proposing that LOR declared as per Appendix A
  This will be further consulted on
LOR levels determined based on load deficits using Uncertainty Margins of different Confidence Levels
The current ‘FUM’ will no longer be used
Confidence Levels used will be consulted with Industry
    AEMO will prepare backcast results showing load deficits at different confidence levels under the proposed methodology as part of the Industry Consultation.
    Ensure in so far as practical that the LOR levels relate to the reliability standards

## Slide 17: Declaration of LOR conditions
Declaration of ‘Actual’ LOR conditions
  ‘Actual’ LOR is based on results of first interval of PD PASA
  Terminology is not ideal as availability is always a forecast not actual
Considering appropriate terminology to be used for declaration of this condition

## Slide 18: Demand Side Participation
AEMO understands DSP will have increasing impact on reserves
Impact of WDR is currently included and will be included in new PD/ST system (the capacity of WDR based on their Max Availability/PASA Availability, similar to treatment of scheduled units)
Other DSP (including price responsive resources, or resources activated by network owners to manage network congestion) will initially be modelled implicitly in the new system via
    The load forecast model, if the activation is correlated with weather conditions or calendar periods or;
    The uncertainty margin, as the activation manifests as forecast error

## Slide 19: Demand Side Participation
Other market initiatives (i.e. scheduled lite*) are expected to deliver visibility and a framework for the treatment of non-scheduled generation and demand, which includes DSP (including price responsive resources). The PD/ST PASA system will be updated accordingly.
*ENERGY SECURITY BOARD Post-2025 Market Design Final advice to Energy Ministers Part B, Page 87, Available here: https://esb-post2025-market-design.aemc.gov.au/reports-and-documents

## Slide 20: Technical Availability for semi-scheduled units
A stakeholder has requested that AEMO publish forward-looking technical availability* for semi-scheduled units
If the AEMC considers it appropriate, AEMO is able to provide this information with the following caveats:
    There is no “reason” field collected or published when participants change their technical availability
    There is no direct field identifying which submission was used in the creation of the UIGF used by PD/ST PASA
      Stakeholders will need to trace the technical availability submission to the pre-dispatch/STPASA run by comparing the offerdatetime of the submission to the rundatetime of pre-dispatch/STPASA
* Technical availability includes Upper MW limit and the elements available information submitted by participants in the EMMS Web Portal

## Slide 21: Latest Indicative timetable
Q4 2021 |  | Q1 2022 |  |  | Q2 2022 |  |  | Q3 2022 |  | ID | Indicative date | Key activity
Nov | Dec | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug |  |  | 
 |  |  |  |  |  |  |  |  |  | 1 | 2 Dec 21 | AEMC draft determination
 |  |  |  |  |  |  |  |  |  | 2 | Dec 21 | Finalise vendor(s) for trial
 |  |  |  |  |  |  |  |  |  | 3 | Q1 2022 | AEMO procedures consultation
 |  |  |  |  |  |  |  |  |  | 4 | 10 Mar 22 | AEMC’s final determination
 |  |  |  |  |  |  |  |  |  | 5 | Q2 2022 | Business requirements complete (including procedures consultation)
 |  |  |  |  |  |  |  |  |  | 6 | TBA | Detailed design and implementation
 |  |  |  |  |  |  |  |  |  | 7 | TBA | Go live
1
AEMC’s draft determination
2
4
Finalise Vendor(s) for trial
AEMC’s final determination
AEMO procedures consultation
commence
3
Business requirements
5

## Slide 22: ‘Go-Live’ date
‘Go-live’ in Q3 2022 is not achievable
AEMO is reviewing the timelines considering:
  Availability of specialised external and internal resources. AEMO is currently considering the RFP responses and timelines provided
  Detailed requirements of external stakeholders as part of the ‘formal’ procedure consultation process
  Timelines required by participants to make changes to their systems to work with the new ST PASA
  Relationship between the ST PASA implementation and IESS, to identify efficiency opportunities e.g., the bidding interface
AEMO has informed the AEMC that the new system may not be in place until at least Q3 2023

## Slide 23: Appendix A (Refresh of proposed design )

## Slide 24: Key themes of HLD
Reliability is a physical system issue hence the model should reflect the physical reality instead of the market
  Full network model
  Forecast at nodal level (load on bus)
Determine uncertainties in demand forecast, VRE forecasts and scheduled unit forced outages
  They become an input into the model (known as ‘Uncertainty Margins’)
  Current ‘FUM’ no longer used

## Slide 25: New PD/ST PASA System

## Slide 26: Determination of Reliability
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48
50 POE Demand | 254.2041 | 257.809 | 265.0187 | 273.6329 | 286.6479 | 299.4287 | 314.5972 | 329.204 | 345.262 | 356.9193 | 366.1421 | 375.5054 | 386.7881 | 397.1345 | 406.2169 | 416.5165 | 429.5783 | 440.112 | 449.9902 | 459.8685 | 468.5763 | 477.0969 | 484.8216 | 491.6568 | 494.0912 | 494.7467 | 486.7879 | 482.3871 | 473.7729 | 461.6007 | 450.1307 | 442.9209 | 427.8461 | 411.039 | 396.76 | 380.6083 | 368.6702 | 354.9998 | 341.4698 | 331.3107 | 322.2751 | 312.7714 | 300.5992 | 290.955 | 283.3239 | 278.0805 | 274.382 | 273.6329
 | Proposed System
Objective | Create generation profile that meets the demand at the node
Subject to | n-1 security constraints (Transmission and generator contingencies)
Demand Used | 50% POE demand + Uncertainty Margin
Reliability Measure | Deficit = Uncertainty Margin + 50% POE Demand - Gen
LOR Declared | Deficit > 0

## Slide 27: Determination of Reliability
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48
50 POE Demand | 254.2041 | 257.809 | 265.0187 | 273.6329 | 286.6479 | 299.4287 | 314.5972 | 329.204 | 345.262 | 356.9193 | 366.1421 | 375.5054 | 386.7881 | 397.1345 | 406.2169 | 416.5165 | 429.5783 | 440.112 | 449.9902 | 459.8685 | 468.5763 | 477.0969 | 484.8216 | 491.6568 | 494.0912 | 494.7467 | 486.7879 | 482.3871 | 473.7729 | 461.6007 | 450.1307 | 442.9209 | 427.8461 | 411.039 | 396.76 | 380.6083 | 368.6702 | 354.9998 | 341.4698 | 331.3107 | 322.2751 | 312.7714 | 300.5992 | 290.955 | 283.3239 | 278.0805 | 274.382 | 273.6329
Uncertanity Margin | 6.5787 | 7.5713 | 7.9906 | 7.8174 | 8.1808 | 9.0152 | 9.4815 | 13.7454 | 15.2287 | 16.5738 | 17.4705 | 38.0729 | 38.6031 | 42.9439 | 44.863 | 51.6545 | 50.0745 | 50.1362 | 50.276 | 46.2432 | 41.8787 | 36.4791 | 36.456 | 36.0549 | 36.0547 | 35.8271 | 35.8991 | 26.5459 | 26.6909 | 25.6321 | 25.7617 | 25.7094 | 25.8168 | 25.1686 | 22.9994 | 21.8655 | 21.3784 | 17.7004 | 15.7224 | 15.62 | 15.3542 | 12.8566 | 12.7417 | 11.3604 | 11.3235 | 10.3783 | 10.4013 | 10.638
 | Proposed System
Objective | Create generation profile that meets the demand at the node
Subject to | n-1 security constraints (Transmission and generator contingencies)
Demand Used | 50% POE demand + Uncertainty Margin
Reliability Measure | Deficit = Uncertainty Margin + 50% POE Demand - Gen
LOR Declared | Deficit > 0

## Slide 28: Determination of Reliability
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48
Dispatched Generation | 260.7828 | 265.3802 | 273.0093 | 281.4503 | 294.8287 | 308.4439 | 324.0788 | 342.9493 | 360.4907 | 373.493 | 383.6125 | 413.5782 | 425.3912 | 440.0784 | 451.0798 | 468.171 | 479.6527 | 490.2482 | 500.2662 | 506.1116 | 510.455 | 510.455 | 510.455 | 510.455 | 510.455 | 510.455 | 510.455 | 508.933 | 500.4638 | 487.2327 | 475.8924 | 468.6303 | 453.6629 | 436.2075 | 419.7594 | 402.4739 | 390.0485 | 372.7002 | 357.1922 | 346.9307 | 337.6293 | 325.628 | 313.3409 | 302.3154 | 294.6474 | 288.4588 | 284.7833 | 284.2709
50 POE Demand | 254.2041 | 257.809 | 265.0187 | 273.6329 | 286.6479 | 299.4287 | 314.5972 | 329.204 | 345.262 | 356.9193 | 366.1421 | 375.5054 | 386.7881 | 397.1345 | 406.2169 | 416.5165 | 429.5783 | 440.112 | 449.9902 | 459.8685 | 468.5763 | 477.0969 | 484.8216 | 491.6568 | 494.0912 | 494.7467 | 486.7879 | 482.3871 | 473.7729 | 461.6007 | 450.1307 | 442.9209 | 427.8461 | 411.039 | 396.76 | 380.6083 | 368.6702 | 354.9998 | 341.4698 | 331.3107 | 322.2751 | 312.7714 | 300.5992 | 290.955 | 283.3239 | 278.0805 | 274.382 | 273.6329
Uncertanity Margin | 6.5787 | 7.5713 | 7.9906 | 7.8174 | 8.1808 | 9.0152 | 9.4815 | 13.7454 | 15.2287 | 16.5738 | 17.4705 | 38.0729 | 38.6031 | 42.9439 | 44.863 | 51.6545 | 50.0745 | 50.1362 | 50.276 | 46.2432 | 41.8787 | 36.4791 | 36.456 | 36.0549 | 36.0547 | 35.8271 | 35.8991 | 26.5459 | 26.6909 | 25.6321 | 25.7617 | 25.7094 | 25.8168 | 25.1686 | 22.9994 | 21.8655 | 21.3784 | 17.7004 | 15.7224 | 15.62 | 15.3542 | 12.8566 | 12.7417 | 11.3604 | 11.3235 | 10.3783 | 10.4013 | 10.638
 | Proposed System
Objective | Create generation profile that meets the demand at the node
Subject to | n-1 security constraints (Transmission and generator contingencies)
Demand Used | 50% POE demand + Uncertainty Margin
Reliability Measure | Deficit = Uncertainty Margin + 50% POE Demand - Gen
LOR Declared | Deficit > 0

## Slide 29: Determination of Reliability
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48
Dispatched Generation | 260.7828 | 265.3802 | 273.0093 | 281.4503 | 294.8287 | 308.4439 | 324.0788 | 342.9493 | 360.4907 | 373.493 | 383.6125 | 413.5782 | 425.3912 | 440.0784 | 451.0798 | 468.171 | 479.6527 | 490.2482 | 500.2662 | 506.1116 | 510.455 | 510.455 | 510.455 | 510.455 | 510.455 | 510.455 | 510.455 | 508.933 | 500.4638 | 487.2327 | 475.8924 | 468.6303 | 453.6629 | 436.2075 | 419.7594 | 402.4739 | 390.0485 | 372.7002 | 357.1922 | 346.9307 | 337.6293 | 325.628 | 313.3409 | 302.3154 | 294.6474 | 288.4588 | 284.7833 | 284.2709
Deficit | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3.1209 | 10.8225 | 17.2567 | 19.6909 | 20.1187 | 12.2319 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
50 POE Demand | 254.2041 | 257.809 | 265.0187 | 273.6329 | 286.6479 | 299.4287 | 314.5972 | 329.204 | 345.262 | 356.9193 | 366.1421 | 375.5054 | 386.7881 | 397.1345 | 406.2169 | 416.5165 | 429.5783 | 440.112 | 449.9902 | 459.8685 | 468.5763 | 477.0969 | 484.8216 | 491.6568 | 494.0912 | 494.7467 | 486.7879 | 482.3871 | 473.7729 | 461.6007 | 450.1307 | 442.9209 | 427.8461 | 411.039 | 396.76 | 380.6083 | 368.6702 | 354.9998 | 341.4698 | 331.3107 | 322.2751 | 312.7714 | 300.5992 | 290.955 | 283.3239 | 278.0805 | 274.382 | 273.6329
Uncertanity Margin | 6.5787 | 7.5713 | 7.9906 | 7.8174 | 8.1808 | 9.0152 | 9.4815 | 13.7454 | 15.2287 | 16.5738 | 17.4705 | 38.0729 | 38.6031 | 42.9439 | 44.863 | 51.6545 | 50.0745 | 50.1362 | 50.276 | 46.2432 | 41.8787 | 36.4791 | 36.456 | 36.0549 | 36.0547 | 35.8271 | 35.8991 | 26.5459 | 26.6909 | 25.6321 | 25.7617 | 25.7094 | 25.8168 | 25.1686 | 22.9994 | 21.8655 | 21.3784 | 17.7004 | 15.7224 | 15.62 | 15.3542 | 12.8566 | 12.7417 | 11.3604 | 11.3235 | 10.3783 | 10.4013 | 10.638
 | Proposed System
Objective | Create generation profile that meets the demand at the node
Subject to | n-1 security constraints (Transmission and generator contingencies)
Demand Used | 50% POE demand + Uncertainty Margin
Reliability Measure | Deficit = Uncertainty Margin + 50% POE Demand - Gen
LOR Declared | Deficit > 0

## Slide 30: Proposal for LOR Levels
Current ST PASA |  | Proposed System | 
Current LOR Levels | Intervene in Market? | Proposed LOR levels | Intervene in Market?
LOR 3 – Cannot meet demand if we have a credible network contingency | Y | LOR RED – Cannot meet demand if we have a credible network contingency OR a credible generator contingency in the NEM Demand = 50 POE demand plus Uncertainty Margin at x%1 confidence level | Y
LOR 2 – Cannot meet demand if we have a credible network contingency OR a trip of the largest generator (in that region) (FUM is also considered at this point) | Y |  | 
LOR 1 - Cannot meet demand if we have a credible network contingency OR a trip of the largest and the second largest generator (in that region) (FUM is also considered at this point) | N | LOR ORANGE – Cannot meet demand if we have a credible network contingency OR a credible generator contingency in the NEM Demand = 50 POE demand plus Uncertainty Margin at y% confidence level (where y>x) | N
 |  | LOR YELLOW – Cannot meet demand if we have a credible network contingency OR a credible generator contingency in the NEM Demand = 50 POE demand plus Uncertainty Margin at z% confidence level (where z>y>x) | N
1 x% is the AEMO intervention level

## Slide 31: Proposal for LOR Levels
Example above would be
LOR RED for Interval 36
LOR ORANGE for Intervals 34,35 & 37
LOR YELLOW for Intervals 33, 38 - 41
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48
50 POE Demand + UM(90) | 6081 | 5879 | 5745 | 5645 | 5566 | 5492 | 5437 | 5410 | 5394 | 5426 | 5465 | 5573 | 5643 | 5832 | 6002 | 6211 | 6320 | 6365 | 6384 | 6445 | 6496 | 6644 | 6835 | 6994 | 7187 | 7383 | 7564 | 7749 | 7956 | 8142 | 8349 | 8556 | 8768 | 8878 | 9000 | 9120 | 8906 | 8766 | 8742 | 8668 | 8488 | 8265 | 7977 | 7630 | 7304 | 6987 | 6721 | 6405
Gen Profile (90) | 6081 | 5879 | 5745 | 5645 | 5566 | 5492 | 5437 | 5410 | 5394 | 5426 | 5465 | 5573 | 5643 | 5832 | 6002 | 6211 | 6320 | 6365 | 6384 | 6445 | 6496 | 6644 | 6835 | 6994 | 7187 | 7383 | 7564 | 7749 | 7956 | 8142 | 8349 | 8556 | 8768 | 8878 | 9000 | 9100 | 8906 | 8766 | 8742 | 8668 | 8488 | 8265 | 7977 | 7630 | 7304 | 6987 | 6721 | 6405
50 POE Demand + UM(95) | 6131 | 5929 | 5795 | 5695 | 5616 | 5542 | 5487 | 5460 | 5444 | 5476 | 5515 | 5623 | 5703 | 5902 | 6082 | 6301 | 6420 | 6475 | 6504 | 6575 | 6636 | 6794 | 6995 | 7164 | 7367 | 7573 | 7764 | 7959 | 8176 | 8372 | 8589 | 8806 | 9028 | 9148 | 9265 | 9269 | 9206 | 9076 | 9062 | 8998 | 8828 | 8615 | 8337 | 7930 | 7574 | 7237 | 6921 | 6545
Gen Profile (95) | 6131 | 5929 | 5795 | 5695 | 5616 | 5542 | 5487 | 5460 | 5444 | 5476 | 5515 | 5623 | 5703 | 5902 | 6082 | 6301 | 6420 | 6475 | 6504 | 6575 | 6636 | 6794 | 6995 | 7164 | 7367 | 7573 | 7764 | 7959 | 8176 | 8372 | 8589 | 8806 | 9028 | 9100 | 9100 | 9100 | 9100 | 9076 | 9062 | 8998 | 8828 | 8615 | 8337 | 7930 | 7574 | 7237 | 6921 | 6545
50 POE Demand + UM(99) | 6181 | 5979 | 5845 | 5745 | 5666 | 5592 | 5537 | 5510 | 5494 | 5526 | 5585 | 5713 | 5803 | 6012 | 6202 | 6431 | 6560 | 6625 | 6664 | 6745 | 6816 | 6984 | 7195 | 7374 | 7587 | 7803 | 8004 | 8209 | 8436 | 8642 | 8869 | 9096 | 9328 | 9458 | 9585 | 9599 | 9546 | 9426 | 9422 | 9368 | 9208 | 9005 | 8737 | 8330 | 8154 | 7787 | 7471 | 7105
Gen Profile (99) | 6181 | 5979 | 5845 | 5745 | 5666 | 5592 | 5537 | 5510 | 5494 | 5526 | 5585 | 5713 | 5803 | 6012 | 6202 | 6431 | 6560 | 6625 | 6664 | 6745 | 6816 | 6984 | 7195 | 7374 | 7587 | 7803 | 8004 | 8209 | 8436 | 8642 | 8869 | 9096 | 9100 | 9100 | 9100 | 9100 | 9100 | 9100 | 9100 | 9100 | 9100 | 9005 | 8737 | 8330 | 8154 | 7787 | 7471 | 7105
Deficit (90) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 20 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Deficit (95) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 48 | 165 | 169 | 106 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Deficit (99) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 228 | 358 | 485 | 499 | 446 | 326 | 322 | 268 | 108 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 32: Appendix B Conceptual Architecture